## Slide 1
Cost Estimation and Quality Surveying of a 5 marla (22.5’ x 50’) House
COST ESTIMATION

## Slide 2
Group Members
Omer Basit
Muhammad Abdullah
Muhammad Ali
Muhammad Sameer
Muhammad Anique

## Slide 3
Performing a detailed estimate of cost and quantities required to build a one story, 05 marla house in Paragone City Housing Scheme, Burki Road, Lahore Cantt.
“
”
OBJECTIVE

## Slide 4
PLAN DETAILS
AREA STATEMENT
Total Area Of Plot = 1125 sq ft
Covered Area Of Ground Floor = 843 sq ft
Open Area of Plot = 208 sq ft
House is a masonry structure. It consists of a bedroom with bath, drawing, lounge, kitchen, powder, porch, lawn at front and an open space at back of house
“
”

## Slide 5
Assumptions and Difficulties Faced
The plan was originally meant for a 2 story house, which was reduced to a single story building.
The type of paint was assumed.
Skirting Height was assumed to be 4".
Tiling Details were assumed.
The unlabelled windows were given dimensions from schedule provided accordingly.
Inclined Wall S7 was assumed short wall.
Boundary Wall Height was assumed 6'.
Tiling Details were assumed.
Plinth Protection Details were assumed.

## Slide 6
Assumptions and Difficulties Faced
Lintel Beam Details was taken from a fellow group due to absence of its details in plan.
Stair Case, Overhead and Underground Water Tank details was excluded from our estimation.

## Slide 7
Excavation Estimate

## Slide 8
DETAILS
Interior Wall Foundation
Section A-A with Foundation Details
Boundary Wall Foundation

## Slide 9
935.516 cft
Total Excavation
Excavation
Excavation
7,130 PKR
Excavation Cost

## Slide 10
Steel Estimate

## Slide 11
01
Roof Slab S1
02
Lintel Beam
03
Beam
Steel Application

## Slide 12
#4/0.5" bars: 23‘
#6/0.75" bars: 30'8“
#3/ 0.375" bars: 23'4"
Steel in Beam

## Slide 13
Total #4 Horizontal Bars: 182.5 ft
Total Stirrups : 105 ft
Steel In Lintel Beam

## Slide 14
#04/0.5" Positive Reinforcement Bar: 3724.25 ft
#04/0.5" Negative Reinforcement Bar: 2165 ft
Steel In Slab

## Slide 15
Steel Schedule
Bar # | Length |  | 
#4 | 6094.75’ | 0.668 lb/ft | 4071.293 lb
#3 | 128’4” | 0.376 lb/ft | 48.253 lb
#6 | 30’8” | 1.502 lb/ft | 46.0613 lb
 |  |  | Σ = 4163.6 lb
Tonnage = 2.083 tons

## Slide 16
4156.61cft
Total Steel
Steel Cost
3,00,910 PKR
Total Steel Cost

## Slide 17
Concrete Estimate

## Slide 18
Estimate for Concrete:
Volume = 915.34 cft
Concrete
2,10,325 PKR
Total Cost

## Slide 19
Masonry Estimate

## Slide 20
Masonry was present in:
Interior wall foundation
Exterior wall foundation
Superstructure
Roof
Masonry

## Slide 21
Volume of Brickwork from FFl till slab: 1101.5085 cft
Volume of Brick blast: 301.019 cft
Volume from foundation till FFL: 1065.228 cft
Volume of Brickwork in roof: 36.627 cft
Total Brickwork: 2504.383 cft
Masonry

## Slide 22
Total Brickwork including mortar: 2203.364 cft
Number of Bricks with Mortar: 27182.4856
Total Bricks: 31998.784 ≈ 32,000
Masonry

## Slide 23
Summary of Brickwork
Structure | Volume
Foundation + Plinth | 1065.228 cft
Super Structure | 1402.532 cft
Roofing | 36.62733125 cft
Total Brick Work | 2504.382587 cft
Total Bricks | 32000 Bricks

## Slide 24
Mortar Estimate

## Slide 25
Wet mortar: 504.455 cft
Dry mortar: 605.3456 cft
Cement: 121.069 cft
Cement Bags: 98.751 ≈ 99 bags
Sand: 484.28 cft
Mortar

## Slide 26
Cost of Brickwork and Mortar
6,29,450 PKR
Total Bricks and
mortar Cost

## Slide 27
Skirting Estimate

## Slide 28
Estimate for Skirting:
Height = 4“
Length(Running) = 235.6842’
Area = 78.5614 sq ft
Skirting

## Slide 29
78.5614 sq ft
Total Area
Skirting
9,650 PKR
Total Skirting Cost

## Slide 30
Tiles Estimate

## Slide 31
Estimate for Tiles:
Provided at Kitchen counter, half the height of kitchen and bathroom walls
Thickness of tile=1 inch
Tiles
14,080 PKR
Total Cost

## Slide 32
Plaster Estimate

## Slide 33
Area of walls to be plaster: 3751.84 cft
Dry Volume of Mortar: 254.036 cft
Cement: 63.51 cft
Cement Bags: 51.8 ≈ 52 bags
Sand: 190.53 cft
Plaster

## Slide 34
Area of roof to be plaster : 604.85 cft
Dry Volume of Mortar: 40.954 cft
Cement: 10.34 cft
Cement Bags: 8.35 bags
Sand: 31.02 cft
Plaster

## Slide 35
Cost of Brickwork and Plaster
93,834 PKR
Total Plaster Cost
7,23,280 PKR
Total Cost of
Bricks and plaster

## Slide 36
Floor and Roof Finishing Estimate

## Slide 37
Estimate for Marble:
Area = 903 sq ft
Floor
1,01,053.6 PKR
Total Cost
Estimate for Sand Filling:
Volume = 490.53 cft
Estimate for Well Compacted Earth:
Volume = 2108.78 cft

## Slide 38
Estimate for ½” Thick Brick Tiles:
Volume = 36.6 cft
Roof
1,01,053.6 PKR
Total Cost
Estimate for Hot Bitumen:
Area = 903.056 sq ft
Estimate for Polythene Sheet:
Volume = 903.056 sq ft
Estimate for Mud Plaster:
Volume = 301.02 cft

## Slide 39
Paint Estimate

## Slide 40
Estimate for Exterior Paint:
Area = 1520.21 sq ft
Paint
74,475 PKR
Total Cost
Estimate for Interior Paint:
Area = 3249.21 sq ft

## Slide 41
4769.42 sq ft
Total Area
Paint
74,475 PKR
Total Paint Cost

## Slide 42
Doors And Windows Estimate

## Slide 43
Estimate for doors and windows:
Woodwork = 119 sft
Glasswork + Aluminium = 115.83 sft
Doors And Windows

## Slide 44
Cost of Doors and Windows
5,09,200 PKR
Total Cost

## Slide 45
D.P.C Estimate

## Slide 46
Estimate for D.P.C:
Area = 11.83 sq ft
D.P.C
60,462 PKR
Total Cost

## Slide 47
Summary Of Estimation
Sr No. | Name Of Item | Quantity | Unit | Rate | Per | Amount In Rupees
1 | Excavation | 935.516 | Cft | 7,623.55 | 1000 cft | 7,128.02
2 | Concrete | 915.34 | Cft | 22,977.75 | 100 cft | 2,10,324.54
3 | Pacca Brick Work In Foundation And Plinth in: (Cement, Sand mortar (1:4)) | 1065.228 | Cft | 27,027.5 | 100 cft | 2,87,904.5
4 | Pain Exterior Coat 2 | 1520.21 | Sq ft | 960.85 | 100 cft | 14,606.94
5 | Pain Exterior Coat 1 | 1520.21 | Sq ft | 1,957.4 | 100 cft | 29,756.6
6 | Pacca Brick Work In Ground Floor: (Cement, Sand mortar (1:4)) | 1402.532 | Cft | 23,707.6 | 100 cft | 3,32,506.7
7 | Pain Interior Coat 2 | 3249.21 | Sq ft | 446.15 | 100 cft | 1,990.5
8 | Pain Interior Coat 1 | 3249.21 | Sq ft | 865.5 | 100 cft | 28,121.9
9 | Wood Work | 119 | Sq ft | 3,774 | Sq ft | 4,49,106
10 | Glasswork + Aluminum | 115.83 | Sq ft | 477 | Sq ft | 55,250.9
11 | Plaster | 4356.69 | Sq ft | 21,53.8 | 100 Sq ft | 93,834.4

## Slide 48
Sr No. | Name Of Item | Quantity | Unit | Rate | Per | Amount In Rupees
12 | Steel | 4828.1 | Lb | 8090.45 | Cwt = 112 lb | 3,00,907.67
13 | Marble | 903.072 | Sft | 9226.45 | 100 sq ft | 83,321.4865
14 | Tiles | 283.2 | Sq ft | 4971.35 | 100 sq ft | 14,078.86
15 | D.P.C | 11.83 | Sq ft | 5112.35 | Sq ft | 60,462.059
16 | Backfilling | 149.712 | Cft | 7623.55 | 1000 cft | 1,141.34
17 | Skirting | 78.56 | Sq ft | 12287.25 | 100 sq ft | 9,657.04
18 | Pacca Brick Work In Roof: (Cement, Sand mortar (1:4)) | 36.63 | Cft | 24667.05 | 100 cft | 9,035.241
19 | Main Gate | 48 | Sq ft | 1251.95 | Sq ft | 60,093.6
20 | Two Coats of Bitumen | 903.1 | Sq ft | 2137.7 | 100 Sq ft | 19,304.63
21 | Two Layers of Polythene Sheet | 903.1 | Sq ft | 10865.9 | 100 Sq ft | 98,125.2
22 | Well Compacted Earth | 2108.8 | Cft | 3516.5 | 1000 cft | 7,415.525
23 | 6” Sand Filling | 490.53 | Cft | 2103.15 | 100 cft | 10,316.5817
Summary Of Estimation

## Slide 49
Total BOQ | 21,84,386.157
Over Head Cost | 3,27,657.9235
Contingencies | 43,687.72
Taxes | 3,05,814.062
Net Total | 28,61,545.866 rupees
Summary Of Estimation

## Slide 50
THANK YOU !!!